## Slide 1: multiScan100 Customer Presentation
Strategic Product Management
December 2022

## Slide 2: multiScan100 Detect, localize and secure - all in one

## Slide 3: Content
Applications
    Fields of applications
    Technology
    Focus application
    LiDAR vs. Camera
Product
    Highlights
    Product positioning
    USP description
    Features / Benefits
    Technology
    Protective field concept
    Variants
    Configuration & Diagnostics
    Accessories

## Slide 4: 1. Applications
    Fields of applications
    Technology
    Focus application
    LiDAR vs. Camera

## Slide 5: Fields of applications
multiScan100
Autonomous Guided Vehicles and service robots
    3D Environmental Perception, Localization and Mapping
    Sensor mounted on the vehicle to support autonomous driving
    Anti-Collision due to environmental perception with broad FOV and 16 scan layers
Anti-Collision and Environmental Perception
Access protection
    Sensor can be used to monitor the presence of objects/persons in a defined volume:
      for security applications (e. g. monitor access to buildings)
      Monitor traffic situations
Stationary applications
Mobile outdoor automation
    3D Environmental Perception in harsh outdoor environment
    Sensor can detect environment and thus control the driving path
    Sensor is constructed to withstand the harsh conditions with e. g. high shock and vibration resistance and IP rating
Anti-Collision and Environmental Perception

## Slide 6: Technology
3D LiDAR
The multiScan100 is based on time-of-flight (TOF) technology
A laser pulse signal is sent out to the object
Laser pulse reflects at an object
The receiver element detects the reflected light
The time from sending to receiving the signal is measured and evaluated and calculated based on the speed of light
By spinning the measurement module and combining it with other measurement modules, a 3D point cloud is calculated
tOS
tSO
Object to be detected

## Slide 7: Mobile Applications
3D Environmental Perception + Localization and Mapping
    All in ONE device
multiScan100

## Slide 8: Mobile Applications
3D Environmental Perception + Localization and Mapping
multiScan100
Upper layers
Upper +42.5° of the field of view
3D Environmental Perception with all layers
More layers looking in front and above the vehicle and not too many layers on the ground

## Slide 9: Mobile Applications
3D Environmental Perception + Localization and Mapping
multiScan100
Lower layers
Lower -22.5° of the field of view for objects on ground level
Detection of smaller obstacles on the ground like fork tines or pallets
Lower layers are used for cliff detection or ramp inclination

## Slide 10: Mobile Applications
3D Environmental Perception + Localization and Mapping
multiScan100
Two high-density layers
0.125° resolution: detect even small objects in far distances due to higher resolution
Horizontal, 0°: Ideal to use for localization and mapping (additional reflector recognition)
Upper, +35°: ceiling can be used for reference measurement since there are fewer changes as on the ground when e. g. racks are moved
Segmented data output, thus reduced latencies – less time blurring
Very good scan field flatness of ±0.5°

## Slide 11: Mobile Applications
multiScan100 – Summary
3D Environmental Perception + Localization and Mapping
    More information about the environment and higher efficiency thanks to the 3D point cloud
2D Localization based on Reflector information
    0° High Resolution-Layer for Localization and Reflector recognition with a range up to 60 m
3D Object detection for Collision avoidance!
    3D Environment perception and Collision avoidance based on a large FoV
Person detection and tracking
    Higher availability with 3D detection of objects and persons

## Slide 12
3D Environmental Perception + Localization and Mapping
    All in ONE device
    ⅔ of the vFOV for anti-collision
      Anti-collision of objects in the front
      Anti-collision of hanging objects
    0° & 35° horizontal high-resolution layer for
      Accurate measuring data for navigation tasks
      Detection of small objects in far distances
    ⅓ of the vFOV for:
      Anti-collision of flat close to the ground obstacle, such as forklift tines or pallets
      Cliff / ramp detection
      Ground reference

## Slide 13: Focus Applications
Why to use the multiScan100 3D LiDAR to solve the applications?
Camera vs. LiDAR
Unique combination of high-density horizontal layers and 3D point cloud
Two layers with 1/8° resolution to detect smaller objects in all distances and the chance to fulfill localization and mapping tasks
Rugged housing and design to suit rough ambient conditions
Variety of SW-Applications and Add-ons to serve customer-specific application
LiDAR vs. Camera – why does LiDAR win?
Bigger field of view (horizontal and vertical) – there is no camera with 360°
Higher ranges due to different technology
Higher robustness against ambient light conditions
High-density measurement data in horizontal scan layers
Increased distance accuracy due to better measurement noise behavior
Camera
multiScan100

## Slide 14: 2. Product
    Highlights
    Features / Benefits
    Specification
    Configuration & Diagnostics
    Accessories

## Slide 15: Highlights
multiScan100
compact
Broad field of view combined with high-density layers
Reliable
Reliable measuring data including multi-echo evaluation
Robust
Rugged design for outdoor environment
Customer Centric
Application-specific sensor setup

## Slide 16: Features / Benefits
multiScan100
High measurement accuracy with less measurement noise. Additional multi-echo technology to increase reliability
Ruggedized design for rough ambient conditions: IP69k, Shock and Vibration resistance
Application-specific sensor setup: selectable measurement module, system plug, Apps and SW Add-ons
a proper identification of obstacles as well as a reliable navigation and mapping with the sensor.
… lead to …
indoor and outdoor usage although having rough ambient conditions.
… enables …
best sensor fit for the required application by only paying for the functions which are really needed.
… result in …
have best of both worlds: high-density layer for navigation and 3D point cloud of the surrounding.
… enable to …
Benefits
Broad field of view (360° x 65°) including two high-density layers with less angular resolution of 0.125° in one device
Features
Robust
Compact
Customer Centric
reliable

## Slide 17: Features / Benefits
multiScan100
With the multiScan100 and the 360° horizontal field of view an obstacle detection around the full vehicle is possible if the sensor is placed correctly (with nothing in front of the sensor)
16 scan layers for dense point cloud and higher chance to detect obstacles
Vertical field of view: -22.5° ... +42.5° leads to the fact that flat objects can be detected on the ground while having a proper scan layer setting for obstacles in front and above the vehicle
High resolution 0° scan layer enables easy navigation purposes and detection of small obstacles even in far distance
Broad field of view (360° x 65°) including two high-density layers with less angular resolution of 0.125° in one device
Feature
have best of both worlds: high-density layer for navigation and 3D point cloud of the surrounding.
Benefit
… enable to …
Advantages
Compact

## Slide 18: Features / Benefits
multiScan100
Objects and persons around the sensor are identified properly
Multi-echo technology generates three echoes per beam to get a higher availability by filtering irrelevant measuring data like rain drops or dust
Segmented data output results in reduced latencies thus less time blurring
Very good scan field flatness of ±0.5° for reliable navigation purposes
High measurement accuracy with less measurement noise. Additional multi-echo technology to increase reliability
Feature
a proper identification of obstacles as well as a reliable navigation and mapping with the sensor.
Benefit
… enables a …
Advantages
reliable

## Slide 19: Features / Benefits
multiScan100
Improved outdoor capabilities with IP65, IP67 and IP69k which means the sensor is completely dustproof and can withstand washdown at pressure
Reliable measurement performance: Shock and Vibration resistance
Measurement filters like rain or particle filter improve the availability and reliability of the sensor because it hides small, irrelevant influences in the measurement data e. g. in a dusty environment, or in rain and snow
Contamination measurement to detect dirt and dust on the sensor
Ruggedized design for rough ambient conditions: IP69k, Shock and Vibration resistance
Feature
indoor and outdoor usage although having rough ambient conditions.
Benefit
… enables …
Advantages
RobusT
IP69k
Standard
Advanced 1
Advanced 2

## Slide 20: Features / Benefits
multiScan100
Configurable sensor concept based on the application requirements (easy configuration by SICK Sales Configurator)
Selectable setup of measurement modules (starting with multiScan100136 - furthers launched in the future)
Selectable system plug (more system plugs available in the future)
Selectable Apps and Software Add-ons (continuous development of new functionalities)
Application-specific sensor setup: selectable measurement module, system plug, Apps and SW Add-ons
Feature
best sensor fit for the required application by only paying for the functions which are really needed.
Benefit
… result in …
Advantages
Customer Centric
Measurement module
Apps & Add-ons
System plug

## Slide 21: Portfolio view
Price
Performance
Safety Line (PL b)
Automation Line
Software
Technology Line
Safety Line (PL d)
*
* Future Option
multiScan100

## Slide 22: The multiScan100
Specification
FOV: 360° x 65° [-22.5° … +42.5°]
Ranges: 10%: 12 m I 90%: 30 m I max. on Reflector: 60 m
Horizontal angular resolution: 0.125° & 1°
Vertical angular resolution: 2.5° & 5°
Scan frequency: 20 Hz I Response time one scan: ≤ 50 ms
Statistical error: ± 50 mm I System. Error: ≤ 20 mm
Beam divergency: 0.3° (Spot size sensor optics cover: 13 mm)
Operating temperature: - 30 … +50 °C
diameter: 100.3 mm
Height: 98.5 mm

## Slide 23: Modular Concept
Configured & software-defined offering
Measurement module
Apps & Add-ons
System plug
Improved customization possibilities
Pre-configuration
Customized connectivity
Pre-mounting
Sales configurator
Application optimized software
Tailored performance
Ease of product selection

## Slide 24: multiScan100
Web server GUI
    Simple and flexible configuration
    Enhanced Diagnostics
    Operating system independent, only web browser is needed
    Standard for upcoming SICK LiDARs to create a common operating entity experience

## Slide 25: Accessories
multiScan100
  Software / web server
    Simple and flexible configuration
    Enhanced Diagnostics
  Cables
    Ethernet connection: M12 4-pin (female connector)
    Power/Synch. output connection: M12 5-pin (male connector)
  Brackets
    Standard bracket
    Alignment bracket
    Fine alignment bracket
    Mounting plate
  Environmental Protection
    Protective optics cover
    Shock absorber

## Slide 26: multiScan100 Detect, localize and secure - all in one
Reliable
Compact
Customer Centric
reliable

## Slide 27: Thank you!
multiScan100

## Slide 28
  Ruggedized design
    Shock & Vibration:
      Advanced 1 & Advanced 2 *
    EMC:
      EN 61000-6-2 & EN 61000-6-3
  Connectivity modular, rotatable, configurable
    System plug concept
    Supported interfaces
      Power 9…30 V DC
      Ethernet TCP/IP & UDP, 100 Mbit/s
      Up to 8 configurable IOs
      Ethernet TCP/IP & UDP, 1 Gbit/s**
      CANopen / SAE J1939**
      Automotive Ethernet 100BASE-T1 / BroadR-Reach**
  Algorithms & Apps
    Web-Server GUI
    Choice of Streaming or / & Field Evaluation App, … and many more!
    Segmented data output
    Multi Echo evaluation (three echo's)
    Reflector recognition
    Advanced filter options
    Diagnosis functions, e.g. screen contamination indication, IMU
    Choice of optimized data formats
    Support of data aggregation tools, e.g.
    Over the Air (OTA) update tool**
multiScan100 overview
Specifications |  | 
Working range | ≤ 0.05 … 60 m2) … 30 m @ 90% … 12 m @ 10% | 
Aperture angle | 360° | 
Field of view | Hor.: 360° Vert.: 65° [-22.5°…+42.5°] | 
Scanning frequency | 20 Hz | 
Angular resolution | Hor.: 0.125° & 1° Vert.: 2.5° & 5° | 
Statistical error (1σ) | ≤ 20 mm | 
Systematic error | ± 50 mm1) | 
Scan field flatness | Nav. layer (0°): ± 0.5° Other layers: ± 1° | 
Ambient light immunity | 100 klx | 
Operating temp. | - 30 … +50 °C / - 40 … +70 °C* | 
Enclosure rating | IP65 & IP67 & IP69k | 
Performance level (in preparation) ** |  | EN ISO 13849-1:2015
1) Depending on range, ambient light, temperature etc. 2) Extended range on reflectors *with accessory ** future options
Notes: IMU: SOPAS Telegram - Polling or continuous streaming

## Slide 29: Durability!
Mechanical robustness levels
Category | LEVEL “advanced 2” | LEVEL “advanced 1”
Vibration resistance | (IEC 60068-2-6:2007) Sine resonance scan: 10…1.000 Hz; 1 g Sine test: 10…500 Hz; 10 g; 10 cycles (IEC 60068-2-64:2008) Noise test: 10…500 Hz, 13.5 gRMS, 5 h | (IEC 60068-2-6:2007) Sine resonance scan: 10…1.000 Hz; 1 g Sine test: 10…500 Hz; 5 g; 10 cycles (IEC 60068-2-64:2008) Noise test: 10…250 Hz, 4.24 gRMS, 5 h
Shock resistance | (IEC 60068-2-27:2008) 100 g, 6 ms; ±3 shocks / axis 40 g, 6 ms; ±4.000 bumps / axis 50 g, 3 ms; ±5.000 bumps / axis | (IEC 60068-2-27:2008) 50 g, 11 ms; ±3 shocks / axis 25 g, 6 ms; ±1.000 bumps / axis 50 g, 3 ms ;±5.000 bumps / axis
How to reach? | Device mounted to SICK shock absorber bracket | Robustness by device design

## Slide 30: Information about Data format
Type | Info | Advantages | Limitations
MSGPCK (data format) | available for UDP and TCP/IP outputs segments (e.g. 30° is one segment) contains information like device Identification / serial number, time stamp and device status requires about ~10 Mbit for picoScan (3 echoes) ~70 Mbit for multiScan100 (3 echoes) | easy to integrate with existing "libraries" Easy to parse ROS drivers also use this protocol Each field has a kind of "speaking name" or numbering | quite a lot of bandwidths requires more computing power, especially for parsing
COMPACT (data format) | available for UDP and TCP/IP outputs segments (e. g. 30° is one segment) similar to other 3D LiDAR Data format approaches contains information like device Identification / serial number, time stamp and device status Requires ~5 Mbit for picoScan (3 echoes) ~35 Mbit for multiScan100 (3 echoes) | very efficient much smaller band with needed "memcpy" will do the job → super efficient and resource-saving a bit like CoLa B | Data is not "self-describing" more "difficult" to parse (needs probably more integration time on customer side)
ROS (driver) | ROS1 & ROS2 | Easy integration, widely used open-source platform | Requires installation of ROS kernel
C++ (driver) |  | Low-level integration, open for a bunch of operation systems and CPU architectures | More complex approach
multiScan100 and other LiDARs

## Slide 31: Measuring data with Quality!
Choice of different data formats & drivers
Type | Info | Advantages | Limitations
MSGPCK (data format) | available for UDP and TCP/IP outputs segments (e.g. 30° is one segment) contains information like device Identification / serial number, time stamp and device status requires about ~10 Mbit for picoScan (3 echoes) ~70 Mbit for multiScan100 (3 echoes) | easy to integrate with existing "libraries" Easy to parse ROS drivers also use this protocol Each field has a kind of "speaking name" or numbering | quite a lot of bandwidths requires more computing power, especially for parsing
COMPACT (data format) | available for UDP and TCP/IP outputs segments (e. g. 30° is one segment) similar to other 3D LiDAR Data format approaches contains information like device Identification / serial number, time stamp and device status Requires ~5 Mbit for picoScan (3 echoes) ~35 Mbit for multiScan100 (3 echoes) | very efficient much smaller band with needed "memcpy" will do the job → super efficient and resource-saving a bit like CoLa B | Data is not "self-describing" more "difficult" to parse (needs probably more integration time on customer side)
ROS (driver) | ROS1 & ROS2 | Easy integration, widely used open-source platform | Requires installation of ROS kernel
C++ (driver) |  | Low-level integration, open for a bunch of operation systems and CPU architectures | More complex approach

## Slide 32: Application software
Modular concept
  “Standard” Sensor Apps
    Measurement data streaming
    Object detection – 2D or 3D **
    &
    & with PL b rating
  Feature Add-ons
    Multi Echo
    Reflector recognition
    Filter package robustness (rain, fog, particles)
    Filter package data reduction & pre-processing
  “Specialized” Sensor Apps
    LiDAR-LOC2 **
    Safe break assist

## Slide 33: Product range (technology)
  multiScan136
    16 scan layers
    2 layers with 1/8° and 14 layers with 1°
    FoV: 65° x 360°
    Range:
      Operating range: 30 m
      extended reflector range up to 60m
  multiScan100-2
    16 scan layers
    16 layers with 1/2°
    FoV: 42.5° x 360°
    Range:
      Operating range: 60 m
  multiScan100-3
    16 scan layers
    16 layers with 1/2°
    FoV: 65° x 360°
    Range:
      Operating range: 60 m
  multiScan136S
    16 scan layers
    2 layers with 1/8° and 14 layers with 1°
    FoV: 65° x 360°
    Range:
      Operating range: 30 m
Q2 / 2023
2
Q3 / 2023
3
tba
4
  multiScan100-4
    8 scan layers
    Horizontal angular resolution: TBD
    FoV: 30° x 360°
    Range:
      Operating range: 60 m
multiScan100 - Roadmap: Version overview
Q1 / 2023
1
tba
5